Tasmota + Berry
Not just for home automation

---
ESP32 SOC
- The ESP32 series of microcontroller by Expressif are a substantial evolution on the ESP8266
- Faster, Dual Core CPU with more memory and many more GPIO
- CPU architecture using the Xtensa LX6 ISA like the ESP8266.
- Some models use the RISC-V ISA
- Addition of Bluetooth on most models
- Many more ADC in addition to DAC and hardware counters
[Speaker Notes: All include 2.4GHz Wifi]

---
ESP Family
	ESP8266	ESP32	ESP32-S2	ESP32-S3	ESP32-C3	ESP32-C6
CPU	Xtensa32Bit	Xtensa32Bit	Xtensa 32 Bit	Xtensa 32bit +	RISC-V 32bit	RISC-V 32bit +
Cores	1	2	1	2	1	1
Clock	80-160MHz	160-240MHz	160-240MHz	160-240MHz	120MHz	160MHz
RAM	160kB	520KB	320KB	512KB	300KB	512KB
Flash	External SPI Flash
Wifi 802.11 b/g/n	✔	✔	✔	✔	✔	+ax +Zigbee
Bluetooth	✘	Classic & BLE	✘	BLE	BLE	Bluetooth5 + LE
GPIO	18	34	34	45	22	22
DAC	✘	2	2	2	✘	✘
ADC	1 10bit	18 12bit	20	20	2	7
Interfaces	SPI-I2C-I2S	✔ +CAN	✔ +CAN	✔ +CAN	✔	✔
[Speaker Notes: There are many variations between models, for instance, ESP32-S3 and C6 include a Low power 20MHz co-processor. More CPU’s are in the pipeline. Expressif have indicated that RISC-V is there long term strategy.]

---
ESP32 Software Support
- Expressif IDF is the official Development Framework
- Arduino support early for ESP8266
- Continued with ESP32
- PlatformIO with VSCode
- Supports most Arduino libraries

---
Tasmota
- Tasmota is an open source firmware for Espressif ESP8266, ESP32, ESP32-S or ESP32-C3 chipset based devices created and maintained by Theo Arends.
- Tasmota grew into a fully fledged ecosystem for virtually any ESP8266/ESP32 based device.
- Tasmota was not designed for Home Assistant, although it grew to interface to it. It is not really comparable with ESPHome.
- A Tasmota device can be stand alone.
[Speaker Notes: Everything began as Sonoff-MQTT-OTA with a commit on 25th January 2016, by Theo Arends. Its goal was to provide ESP8266 based ITEAD Sonoff devices with MQTT and 'Over the Air' or OTA firmware. What started as a simple way to hack a cloud bound Sonoff Basic (one of the first cheap and accessible smart home devices in the market) into a locally controlled device has grown into a fully fledged ecosystem for virtually any ESP8266/ESP32 based device.]

---
ESP8266 Tasmota Design
- Peripheral Device drivers and configuration to assign GPIO
- Wifi with Over the Air upgrade capability.
- MQTT support
- Comprehensive command set
- Rule Engine
- Capacity limits of ESP8266 meant that there were many different images to support the required functions.
[Speaker Notes: The ESP8266 storage and memory limits meant that all possibe features could not be supported at once. Indeed, an OTA upgrade involves 2 steps. First step loads a minimal image, then the full image is installed over it.]

---
Commands and Rules
- Command
- Rule
- There are other triggers depending on the peripherals configured
POWER1 ON
websend [192.23.1.20] power1 0
ON POWER1#STATE=1 DO RULETIMER1 600 ENDON
ON RULES#TIMER=1 DO POWER1 0 ENDON
ON ANALOG#A0div10 DO DIMMER %value% ENDON
[Speaker Notes: In the command example. Assuming a relay has been configured. POWER1 ON turns on the first relay Using websend allows peer to peer commands An example rule When POWER1 is turned on a timer is loaded with 600 (seconds) When the timer expires the relay is turned off When ANALOG A0 changes more than 1% adjust the dimmer by the returned value These examples do not need anything else to operate.]

---
Road to ESP32
- A scripting engine that worked with Tasmota was needed:
  - General purpose programs
  - Ability to write device drivers without recompiling
- Review of options
  - Micropython - took over the machine
  - LUA - heavyweight and obscure syntax
  - https://github.com/cesanta/elk – Javascript Syntax
  - Berry – Python Syntax
[Speaker Notes: Write conventional programs with normal language construction Device drivers need to interface closely with Tasmota which is providing the usual infrastructure Micropython would replace Tasmota LUA consumed to much resources In the end, the choice came down to the developer preferred pythonese to java script]

---
Berry
- Lightweight: A well-optimized interpreter with very little resources.
- Fast: optimized one-pass bytecode compiler and register-based virtual machine.
- Powerful: supports imperative programming, object-oriented programming, functional programming.
- RAM saving: RAM usage starts at ~10kb
- Additional libraries provided, with deep hooks into Tasmota
- Tasmota incorporates a Web based UI to Berry
[Speaker Notes: Berry is just a library and berry programs are called within the Tasmota event loop. Tasmota hands control to the Berry until a call is made back into Tasmota. Poorly written Berry programs can take prevent Tasmota performing the other functions, so an event mechanism is required.]

---
- Berry Scripting console
- Berry code saved to filesystem, can be loaded at startup
[Speaker Notes: Berry code can be executed from the Berry console, much like python.]

---
Program Execution
- Berry programs in the filesystem can be executed
  - by the load() function from the Berry console
  - Run at startup if named ‘autoexec.be’ which can the load() other files.
  - From the Tasmota console using the ‘br’ command
  - From a tasmota rule
ON Time#Minute=0 DO br load(“midnight.be”) ENDON
ON DS18B20#Temperature<10
DO WEBSEND[192.168.10.3] br load(“TooCold.be”)
[Speaker Notes: The load() function looks for that filename or with a .be extension, loads and executes. If the program has not been loaded previously, it is compiled to bytecode then executed. The bytecode is stored as the filename with a .bec extension. This also applies if the file is newer than the bytecode file. Berry VM can be restarted with the ‘brrestart’ console command]

---
Support Libraries
- Berry has a number of modules that can be imported as required:
  - String
  - JSON
  - MATH
  - MQTT
  - Tasmota
  - GPIO
[Speaker Notes: String library contains the usual string functions, formatting, counting occurrences,search etc JSON library contains function for serialising and deserialising JSON strings. Very useful as tasmota returns a lot of JSON strings from calls. MATH MQTT (publishing and subscribing) Tasmota contains many functions and classes for getting data and manipulating tasmota internals.]

---
Tasmota module
- Send a command to Tasmota
- Create a Tasmota command written in Berry
- Timers
tasmota.cmd(“dimmer 60”)
def hello_from_berry()
print(“Hello from Berry”)
end
tasmota.add_cmd(“hello”,hello_from_berry)
tasmota.set_timer(600,hello_from_berry)
tasmota.add_cron("*/10 * * * * *",hello_from_berry)

---
Tasmota module
- add_rule()
- read_sensors()
- get_power() / set_power() / get_switches()
- url_get()
- rtc()/time_str()
- ...

---
Tasmota Module (Driver)
- Berry can be used to add device drivers
- Override driver class methods as required
- Add fast_loop() to Tasmota main loop
  - fast_loop function called 200 times/sec
class MyDriver
  def every_second()
    # do something
  end
end
d1 = MyDriver()
tasmota.add_driver(d1)
[Speaker Notes: Class methods include every_second() every_250ms() every_100ms() web_sensor() fast_loop() needs to be registered separately]

---
Driver with fast_loop
class my_driver
def every_100ms()
    # called every 100ms via normal way
  end
  def fast_loop()
    # called at each iteration, and needs to be registered separately and explicitly
  end
  def init()
    # register fast_loop method
    tasmota.add_fast_loop(/-> self.fast_loop())
  end
end
tasmota.add_driver(my_driver()) # register driver
[Speaker Notes: Example from the documentation showing the overridden every_100ms() method The Fast_loop() is added in the class init() method The / arrow is the creation of a closure, in Berry a closure is best explained as a synthetic function.]

---
Other Modules
- MQTT
  - Subscribe and publish MQTT messages
- GPIO
  - Perform operations on GPIOs
  - Read and write hardware counters
- WIRE
  - I2C bus operations
- PERSIST
  - Manage persistent data
[Speaker Notes: Publish to Tasmota configured MQTT Server Subscribe to a topic which calls a Berry function on receipt Direct access to GPIO, bypassing tasmota I2C bus devices for device drivers Persistent data written to a file in JSON format]

---
Home Automation?